## Slide 1
Investigation of Advanced Modulation Formats
for Terabit Short Reach Optical
Communication Systems
Majidah Hameed Majeed
By
Majidah Hameed Majeed
28-12-2017

## Slide 2
Contents
Aim of the work
Conclusions
Investigation, design and simulation of 112 Gb/s multiband CAP/QAM system
Future work
Majidah Hameed Majeed
CAP modulation: Problem definition, CAP modulator
Introduction
Investigation, design, and simulation of extended 1.8 Tb/s system
Applications

## Slide 3
Aim of the work
Investigate + analysis of terabit transmission for short reach optical communication systems
Simulate the performance of the systems using OptiSystem 14.0
Investgate CAP/QAM system
Derive mathematical expressions of the system using
CAP transmitter
QAM or CAP receiver
Specify simulation Parameters
Design +analysis of 112 Gb/s optical communication system based CAP format
Theoretical modeling framework and performance assessment
1
2
Investigate, plan the careful consideration in performing and setting the accurate values of the parameters for WDM to simulate the extended system
100 GHz channel spacing
200 GHz channel spacing
Present the design and investigation of 1.8 Tb/s WDM system based on multiband CAP-16 using 16 CW lasers and SMF operating at C band and O band to be compared with that of single-band

## Slide 4
. When the number of different services of the users and access chances are increased, the high speed of local area network (LAN) interfaces such like 40 GbE and 100 GbE are needed.
Introduction
Over the last decades, the users’ needs have been varied from emails and commercial dealing documents to extended broadband access.
The demand for 100 Gb/s transmission capacity has been strengthened by the expectations of 40/100 Gigabit Ethernet (GbE).

## Slide 5
Introduction to short reach-optical communication system
Majidah Hameed Majeed
Core networks join towns (long-haul)
Access networks transfer data between users
Metro networks urban states
as a bridge between core & access
Critical roll in data center communications.
Growing bandwidth demand is much more
than that of long-haul.
Key considerations;
Power & cost efficiency and transmission performance

## Slide 6
Simpler DSP does not
require ADC or DAC
It neither requires DFT as
compared to OFDM
nor complex mixer and
LO compared to QAM
Problem: extra bit
rate, low power
and low cost
CAP is of Spectral efficiency
Solution
PAM limits its SE, high number
of levels are affected by noise.
PAM affected by nonlinear
transfer function of modulator.
PAM affected by CD & LP channel charactersitic
Data
S/P
Q-Tx. Filter
I-Tx. Filter
Q-Tx. Filter
I-Tx. Filter
PAM mapper
PAM mapper
PAM mapper
PAM mapper
It supports single laser
100 Gb/s IM/DD optical link
Subbands of MB-CAP are of different , lower symbol rate, power may be adapted to each sub-band SNR. Then overcomes the significant defect of SB-CAP (flat frequency response) then MB-CAP lowers PAPR.
MB-CAP

## Slide 7
0 1 1 0
0 1 1 0 1 0 11110001001111
100010
Mapper
1 0 111

## Slide 8
0 1 1 0
0 1 1 0 1 0 11110001001111
100010
CAP modulator
1 0 111
SRRC shaping filters

## Slide 9
It is of excellent performance using low cost limited bandwidth DML and VCSEL lasers.
Majidah Hameed Majeed
Advantages of CAP modulation
Data
S/P
Q-Tx. Filter
I-Tx. Filter
Q-Tx. Filter
I-Tx. Filter
PAM mapper
PAM mapper
PAM mapper
PAM mapper
PD
Data
P/S
Clock recovery
Offline Processing
QAM Demodulator
QAM de-mapper
Clock recovery
Decision
Offline Processing
Clock recovery
Clock recovery
QAM Demodulator
Decision
QAM de-mapper
SMF
MZM
CW Laser
Transmitter
Receiver
It increases the SE by increasing the order of modulation.
Since CAP format is of high bandwidth efficiency low implementation costs.
It allows high data rate.

## Slide 10
Effect of Roll-off Factor
Effect of Number of Subbands
Maximum Allowable Distance
CAP-16/QAM-16
CAP-32/QAM-32
CAP-64/QAM-64
Effect of Operating Wavelength
Effect of Roll-off Factor
Effect of Modulation Order
4 Subbands
8 Subbands
16 Subbands
Majidah Hameed Majeed
Investigation, design and simulation of 112 Gb/s multiband CAP/QAM system

## Slide 11
MB-CAP TX1
MZM
CW Laser
…
SMF
PD
MB-QAM RX1
LPF
…
…
…
PD
LPF
PD
LPF
WDM Multiplexer
WDM De-Multiplexer
MB-QAM RX2
MB-QAM RX16
MB-CAP TX2
MZM
CW Laser
MB-CAP TX16
MZM
CW Laser
Investigation, design and simulation of 1.8 Tb/s extended system

## Slide 12
Applications
The multimedia services and cloud computed requirements.
CAP has been widely used in asynchronous digital subscriber link and asynchronous transfer mode local area network.
Data-center applications among which are high quality television, video-on-demand online gaming, and high speed internet.
High speed of local area network (LAN) interfaces.

## Slide 13
Thank you for Your Listening