## Slide 1: Device Selection and Data Transfer
The objective of selecting an output device is to get information or a result out of the processor and store it or display it.
The OUT instruction serves that purpose. During the execution of this instruction, the processor places that information (accumulator contents) on the data bus.

## Slide 2: Interfacing of microprocessor
A microprocessor would not be of much use by itself. To perform useful work it needs to be connected to other electronic components. For example, for a computer to work, a microprocessor must be interfaced to main memory, a graphic subsystem, disk memory, the keyboard and USB ports, etc.
There are two types of interfacing:
Memory interfacing.
I/O interfacing.

## Slide 3: Interfacing of microprocessor
Memory interfacing:
While executing an instruction, there is a necessity for the microprocessor to access memory frequently for reading various instruction codes
and data stored in the memory. The primary
function of a memory interfacing circuit is to aid the microprocessor in reading and writing a data to the given register of a memory chip.

## Slide 4: Interfacing of microprocessor
I/O Interfacing:
We know that keyboard and Displays are used as
communication channel with outside world. So it
is necessary that we interface keyboard and displays with the microprocessor. This is called I/O interfacing.

## Slide 5: Memory interfacing
There needs to be a lot of interaction between the microprocessor and the memory for the exchange of information during program execution.
  Memory has its requirements on control
signals and their timing.
  The microprocessor has its requirements as well.
The interfacing operation is simply the matching of these requirements.

## Slide 6
Memory interfacing
Accessing memory can be summarized into the following three steps:
Select the right memory chip (using part of the address bus).
Identify the memory location (using the rest
of the address bus).
Access the data (using the data bus).

## Slide 7: The Design and Operation of Memory
Memory in a microprocessor system is where information (data and instructions) is kept. It can be classified into two main types:
  Main memory (RAM and ROM)
  Storage memory (Disks , CD ROMs, etc.)
The simple view of RAM is that it is made up of registers that are made up of flip-flops (or memory elements).
  The number of flip-flops in a “memory register” determines the size of the memory word.
ROM on the other hand uses diodes instead of the flip- flops to permanently hold the information.
7

## Slide 8
Memory structure & its requirements
The way of interfacing the above two chips to the microprocessor is the same. However, the ROM does not have a WR signal.
Lines
Date Lines
RD
ROM
Address
Lines
Data Lines
CS
RD
Output Buffer
RAM
WR
Input Buffer
 | Output Buffer |  |  | 
Data Lines

## Slide 9
Putting all of the concepts together:
Back to the Overall Picture
•
A15-A8
Latch
AD7-AD0
D7- D0
A - A
7 0
ALE
WR RD IO/M
1K Byte Memory Chip
WR
RD
A9- A0
A15- A10
8085
CS
Chip Selection Circuit | 

## Slide 10: Tri-State Buffers
An important circuit element that is used widely in memory.
This buffer is a logic circuit that has three states:
  Logic 0, logic1, and high impedance.
  When this circuit is in high impedance mode it looks as if it is disconnected from the output completely.
The Output is Low
The Output is High
High Impedance

## Slide 11: The Tri-State Buffer
This circuit has two inputs and one output.
  The first input behaves like the normal input for
the circuit.
  The second input is an “enable”.
    If it is set high, the output follows the proper circuit behavior.
    If it is set low, the output looks like a wire connected to
nothing.
Input
Output
Enable
Input
Output
Enable
OR

## Slide 12: The Basic Memory Element
The basic memory element is similar to a D latch.
This latch has an input where the data comes in.
It has an enable input and an output on which
data comes out.
Data Input
utput
 | D Q EN | Data O
Enable |  | 

## Slide 13: The Basic Memory Element
However, this is not safe.
Data is always present on the input and the output is always set to the contents of the latch.
To avoid this, tri-state buffers are added at the input and output of the latch.
Data Input Data Output
D Q
Enable
EN
WR
RD

## Slide 14: The Basic Memory Element
The WR signal controls the input buffer.
The bar over WR means that this is an active low signal.
So, if WR is 0 the input data reaches the latch input.
If WR is 1 the input of the latch looks like a wire connected to nothing.
The RD signal controls the output in a similar manner.

## Slide 15: A Memory “Register”
If we take four of these latches and connect them together, we would have a 4-bit memory register.
WR
RD
EN
Q
D
EN
Q
D
EN
Q
D
EN
Q
D
EN
I0
I1
I2
I3
O0
O1
O2
O3

## Slide 16: A group of memory registers
Expanding on this scheme to add more memory registers
we get the diagram to the right.
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D0
D1
D2
D3
D0
D1
D2
D3
o
o
o
o
o
o
o
o
WR
RD

## Slide 17: A group of Memory Registers
– If we represent each memory location (Register) as a block we get the following
I0 I1 I2 I3
WR
EN0 EN1 EN2 EN3
RD
O0 O1 O2 O3
 | Input Buffers |  |  |  | 
 | Memory Reg. 0 |  |  |  | 
 | Memory Reg. 1 |  |  |  | 
 | Memory Reg. 2 |  |  |  | 
 | Memory Reg. 3 |  |  |  | 
 | Output Buffers |  |  |  | 

## Slide 18: The Design of a Memory Chip
Using the RD and WR controls we can determine the direction of flow either into or out of memory. Then using the appropriate Enable input we enable an individual memory register.
This memory would be called 4 X
location X number of bits per location].
4 [Number of
What we have just designed is | a | memory | with 4
locations and each location has | 4 | elements | (bits).

## Slide 19: The Enable Inputs
How do we produce these enable line?
– Since we can never have more than one of these enables active at the same time, we can have them encoded to reduce the number of lines coming into the chip.
– These
encoded
lines
are the address
lines for
memory.

## Slide 20: The Design of a Memory Chip
– So, the previous diagram would now look like the following:
I0 I1 I2 I3
Input Buffers
Output Buffers
Memory Reg. 0
Memory Reg. 1
Memory Reg. 2
Memory Reg. 3
O0 O1 O2 O3
WR
RD
A
d d r e s s
D
e c o d e r
A1
A
0

## Slide 21: The Design of a Memory Chip
Since we have tri-state buffers on both the inputs and outputs of the flip flops, we can actually use one set of pins only.
– The chip would now look like this:
Input Buffers
Output Buffers
Memory Reg. 0
Memory Reg. 1
Memory Reg. 2
Memory Reg. 3
WR
RD
A
d d r e s s
D
e c o d e r
A1
A
0
D0 D1 D2 D3
D0 D1 D2 D3
A1
A
0
RD WR

## Slide 22: Dimensions of Memory
Memory is usually measured by two numbers: its length and its width (Length X Width).
  The length is the total number of locations.
  The width is the number of bits in each location.
The length (total number of locations) is a function
of the number of address lines.
# of memory locations = 2( # of address lines)
  So, a memory chip with 10 address lines would have
210 = 1024 locations (1K)
  Looking at it from the other side, a memory chip with 4K locations would need
Log2 4096=12 address lines

## Slide 23: The 8085 and Memory
The 8085 has 16 address lines. That means it can address
216 = 64K memory locations.
– Then it will need 1 memory chip with 64 k locations, or 2 chips with 32 K in each, or 4 with 16 K each or 16 of the 4 K chips, etc.
How would we use these address lines to control
the multiple chips?

## Slide 24: Chip Select
Usually, each memory chip has a CS (Chip Select) input. The chip will only work if an active signal is applied on that input.
To allow the use of multiple chips in the make up of memory, we need to use a number of the address lines for the purpose of “chip selection”.
– These address lines are decoded to generate the
2n
necessary CS inputs for the memory chips to
be used.

## Slide 25: Chip Selection Example
Assume that we need to build a memory system made up of 4 of the 4 X 4 memory chips we designed earlier.
We will need to use 2 inputs and a decoder to
identify which chip will be used at what time.
The resulting design would now look like the one on the following slide.

## Slide 26: Chip Selection Example
CS
RD WR
A0 A1
CS
RD WR
A0
A1
CS
RD WR
A0 A1
CS
RD WR
A0 A1
A3
A2
A0 A1
RD
WR
D0 D1
 | 2 X4 Decoder

## Slide 27: Memory Map and Addresses
The memory map is a picture representation of the address range and shows where the different
memory chips
range.
0000
are located within the address
0000
Address Range
A3FF A400
Address Range of 4th RAM Chip
F7FF FFFF
Address Range of EPROM Chip
3FFF
4400
Address Range of 1st RAM Chip
5FFF
6000
Address Range of 2nd RAM Chip
8FFF
9000
Address Range of 3rd RAM Chip
EPROM
RAM 1
RAM 2
RAM 3
RAM 4

## Slide 28: The 8085 and Address Ranges
The
8085 has 16 address lines. So,
it can
address a total of 64K memory locations.
If we use memory chips with 1K locations each,
then we will need 64 such chips.
The 1K memory chip needs 10 address lines to
individually identify the 1K locations. 10)
(log21024 =
– That leaves 6 address lines which is the exact number needed for selecting between the 64 different chips (log264 = 6).

## Slide 29: The 8085 and Address Ranges
Now, we can break up the 16-bit address of the 8085 into two pieces:
A15 A14 A13 A12 A11 A10 A9 A8 A7 A6 A5 A4 A3 A2 A1 A0
Chip Selection Location Selection within the Chip
– Depending on the combination on the address lines A15 - A10 , the address range of the specified chip is determined.

## Slide 30: Chip Select Example
A chip that uses the combination A15
- A10 =
001000 would have addresses that range from
2000H to 23FFH.
Keep in mind that the 10 address lines on the chip gives a range of 00 0000 0000 to 11 1111 1111 or 000H to 3FFH for each of the chips.
The memory chip in this example would require the following circuit
on its chip select input:
CS
A10
A11
A12
A13
A14
A15

## Slide 31: Chip Select Example
If we change the above combination
to the
following:
Now the chip would have addresses ranging from: 2400 to 27FF.
Changing the combination of the address bits connected to the chip select changes the address range for the memory chip.
CS
A10
A11
A12
A13
A14
A15

## Slide 32: Chip Select Example
To illustrate this with a picture:
  In the first case, the memory chip occupies the piece of
the memory map identified as before.
  In the second case, it occupies the piece identified as after.
Before After
0000 0000
2000
23FF
FFFF
2400
27FF
FFFF

## Slide 33: High-Order vs. Low-Order Address Lines
The address lines from a microprocessor can be classified into two types:
  High-Order
    Used for memory chip selection
  Low-Order
    Used for location selection within a memory chip.
  This classification is highly dependent on the memory system design.

## Slide 34: Data Lines
All of the above discussion has been regarding memory length. Lets look at memory width.
We said that the width is the number of bits in each
memory word.
  We have been assuming so far that our memory chips have the right width.
  What if they don’t?
It is very common to find memory chips that have only 4 bits per location.
How would you design a byte wide memory system using these chips?
We use two chips for the same address range. One chip will supply 4 of the data bits per address and the other chip supply the other 4 data bits for the same address.

## Slide 35: Data Lines
CS
A0
… A9
CS
CS
D0
… D3
D4
…
D7